KERMIT-09 Users guide


                            FLEX-09 KERMIT
                            --------------




     Author:      Jur van der Burg
                  Nettelhorst 56
                  2402 LS  Alphen aan den Rijn
                  The Netherlands
     Language:    C (Compiled with Introl (c) compiler)
     Version:     2.3
     Date:        November 1985




     KERMIT for FLEX is derived from the UNIX version.
     It is enhanced in several ways, such as data logging, server
     mode etc.

     It  should  run  on  about  any  version of the FLEX-09 (tm)
     operating  system. Hardware dependent things are kept in the
     files FLK.H and FLIO.C .

























Š     KERMIT-09 Users guide

     Command summary:

     CONNECT
          Format:   CONNECT

     The  CONNECT  command will allow you to make a connection to
     the  remote  system  over the line that was specified by the
     SET  LINE  command.  If a log file was opened (SET LOG) then
     the  data  will be buffered in memory. If this becomes full,
     it will be written to disk. Handshaking is provided (see SET
     HANDSHAKE).
     While connected, several sub-commands are possible.
     These are the escape character arguments:

          C            Close connection, "escape" to command mode
          S            Show status of connection
          Q            Quit logging
          R            Resume logging
          H            Show availability
          B            Send 'BREAK' signal
          F            Execute FLEX command
          0            Send null
          ?            Show escape character arguments
          escape char  Send escape character itself
          Other        Rings the bell


     SEND
          Format:    SEND file [,file [,file...]]

     The  SEND  command  will  allow you to send a file(s) to the
     other   Kermit.  The  drive  number  specification  will  be
     stripped off the filespec.
     The current transfer can be aborted with control-C.


     RECEIVE
          Format:    RECEIVE

     The RECEIVE command will allow you to receive a file(s) from
     the  other  Kermit.  The  filenames will be specified by the
     sending (remote) Kermit.
     The current transfer can be aborted with control-C.


     GET
          Format:    GET file [,file [,file...]]

     The  GET  command  will  allow  you  to get a file(s) from a
     remote server by specifying their names.
     The current transfer can be aborted with control-C.

Š     KERMIT-09 Users guide

     SERVER
          Format:    SERVER

     This  command  will  cause  Kermit to enter server mode. The
     other  Kermit  can  then  issue  server commands to send and
     receive  files  without  having  to  give  SEND  or  RECEIVE
     commands  to  Kermit-09. Type a Control-C to quit the server
     mode. After a timeout the server will quit.


     FINISH
          Format:    FINISH

     This  command  will  case Kermit-09 to tell the other Kermit
     (Which  should be in server mode) to exit from Kermit. After
     receiving  acknowledgement  that  this is being done, Kermit
     will prompt for another command.

     BYE
          Format:    BYE

     This  command  will cause Kermit-09 to tell the other Kermit
     (which should be in server mode) to exit from Kermit and, if
     applicable,  terminate  its  job  (or  process, etc.). After
     receiving  acknowledgement  that  this is being done, Kermit
     will exit to FLEX.


     HELP
          Format:    HELP

     This  command  will  give  a  short display of the available
     commands.


     LOAD
          Format:    LOAD file

     This command will send a textfile to the current line.
     It  can  be  used  to  send  a file of parameters to a smart
     modem, or to send bare text to the remote system.


     FLEX
          Format:    FLEX [command]

     This  command  allows  you  to  execute  a FLEX command from
     within Kermit. When no command is given, it will be prompted
     for.  Be  careful only to use FLEX commands which run in the
     utility command space!


Š     KERMIT-09 Users guide


     STATUS
          Format:    STATUS

     This  command  shows  the  current status of Kermit-09. This
     includes  the  number  of characters that have been send and
     received  from  the remote Kermit. When a real-time clock is
     available,  an  estimate  of  the effective baud rate of the
     transfer is included.


     EXIT
          Format:    EXIT

     This  command  will  exit  Kermit-09. If a log file was used
     with  CONNECT,  and the buffer contains still data, then the
     buffer will be written to disk before terminating Kermit-09.



































Š     KERMIT-09 Users guide


     The SET command is used to set various parameters in Kermit.

     SET
          Format:    SET command


     LINE
          Format:    SET LINE address

     This  command  will the the address of the interface you are
     using  for  the transfer. A check will be made to see if the
     interface is available.

     BAUD
          Format:    SET BAUD speed

     This   command   will  set  the  desired  baudrate  for  the
     communication.  In  simple  FLEX  systems the only baudrates
     allowed are 300 and 1200. This is switched by the divider of
     the ACIA interface.


     CONFIGURATION
          Format:    SET CONFIGURATION number

     This  command  will  set  the  configuration  to use for the
     communication. The following values are possible:

     0 - 7 bits, even parity, 2 stop bits
     1 - 7 bits, odd parity, 2 stop bits
     2 - 7 bits, even parity, 1 stop bit
     3 - 7 bits, odd parity, 1 stop bit
     4 - 8 bits, no parity, 2 stop bits
     5 - 8 bits, no parity, 1 stop bit
     6 - 8 bits, even parity, 1 stop bit
     7 - 8 bits, odd parity, 1 stop bit


     ESCAPE

          Format:    SET ESCAPE character

     This  command allows you to set the ESCAPE character for the
     CONNECT processing.


     DEBUG
          Format:    SET DEBUG on/off

     This  command  will  make the transfer more verbose. It will
     show the received and transmitted packets, and various other
     things of interest.Š     KERMIT-09 Users guide



     TIMEOUT
          Format:    SET TIMEOUT value

     This command will set the number of seconds before Kermit-09
     will  time out to attempt to receive a message. This timeout
     is  used  to handle transmission errors which totally lose a
     message. The default value is five seconds.


     IMAGEMODE
          Format:    SET IMAGEMODE on/off

     This  command will set the image mode transfer flag. When it
     is  set,  the  data  will  be  transferred as it is. This is
     useful  for transfer between FLEX systems. When clear, space
     compression  will take place, as well the expansion of tabs.
     Carriage  returns  will  not  be processed, while a linefeed
     will be converted to a carriage return.


     DUPLEX
          Format:    SET DUPLEX full/half

     This  command  will control the CONNECT command, in that the
     locally  typed  characters will be echoed to te local system
     when duplex is set to HALF.


     LOG
          Format:    SET LOG file

     This  command  will  specify  a  file  to  capture  the data
     received from the remote system within the CONNECT command.
     The file will be closed if the filespec is a dash ('-').


     HANDSHAKE
          Format:    SET HANDSHAKE start stop

     This  command  will  set  the  handshake characters used for
     controlling  data  within  the CONNECT command. The defaults
     are  XON and XOFF. When the capture buffer becomes full, the
     stop  character is sent to the remote system. If that system
     stops  sending  data,  the  buffer  will be written to disk.
     After that the start character will be sent.

     The  SHOW  command will show all parameters set with the SET
     command, with one extension: SHOW ALL.

          Format:    SHOW command