------------------------------------------
Inside the STE Part1 - Introducing the STE
Copyright c.1991 A Greenwood 
------------------------------------------

     There  is  little doubt that Atari's STE  is  a  significant 
improvement to the successful ST range, but many people are still 
unsure as to what this relatively new machine has to offer. As an 
introduction to a series of articles on programming the STE, this 
article  explains just what Atari have  added.  Further  articles 
will  explain the tricks and techniques needed to  program  these 
extra  features,  with documented 68000 source code  for  example 
programs and STE utilities.

     Overall,  Atari made improvements in seven main areas on the 
STE:

1. A new version of TOS, version 1.6 or 1.62
2. The addition of the Blitter chip previously found on Mega STs
3. A new DMA sound chip with volume and tone control
4. An improved video shifter chip.
5. A Cookie Jar to allow programmers to identify the machine.
6. Two new ports supporting four extra joysticks plus paddles.
7. Use of SIMM cards for easier memory expansion.

------------------
TOS 1.6 (and 1.62)
------------------
     This  version of TOS includes all the features of  TOS  1.4, 
the latest version of TOS for the ST,  but is slightly  different 
internally  to allow for the new hardware.   The main  difference 
from  a user's point of view is the inclusion of a menu  item  to 
allow  use of the blitter chip to be selected from  the  desktop, 
and  the resulting improvements in speed when the blitter is  on. 
Other enhancements,  such as the new file selector and the MS-DOS 
compatible  disc format,  are the same as for TOS  1.4,  and  are 
explained  in the STE addendum sheet supplied with  the  machine. 
TOS 1.62 is just TOS 1.6 with the bugs which were present in  the 
original STEs corrected.

     On the programming side,  this version of TOS can be treated 
exactly as TOS 1.4, with the same additions to the GEM libraries. 
The  changes made to accomodate new hardware are  transparent  to 
the  programmer,  ie  they do not affect the  way  the  operating 
system  appears  compared  to  TOS  1.4.   For  most   commercial 
programming  languages,  for  instance Devpac 2  and  Lattice  C, 
updated  libraries  and macros for using the new  GEM  calls  are 
included in versions released after the new TOS.

------------
Blitter Chip
------------
     All  STEs  have  Atari's Blitter  chip  as  standard,  where 
previously it was only found on the Mega STs. The Blitter chip is 
a  direct  memory access (DMA) device which uses the STs  bus  to 
transfer  data directly from one part of memory to  another  more 
quickly than is possible using the 68000 processor.  It does this 
by  using the DMA controller to take control of the 68000's  bus, 
either  in  bursts  interleaved  with the CPU  or  until  it  has 
finished. In this way the Blitter chip can be used instead of the 
processor for fast movement of data.

     The  Blitter  chip can also manipulate the data  in  several 
ways as it is transferred.  Since data transfer is bit  oriented, 
the  source data can be shifted to produce the destination  data, 
previously  one  of  the hardest  parts  of  bit-mapped  graphics 
programming.  The  Blitter  also  applies  one  of  16  different 
combinations of logical operations to the source data  (including 
straight copy,  of course),  and can also combine the source data 
with 16 word length half-tone RAM registers for special effects.

     When  copying  data the Blitter chip can  skip  a  specified 
number  of bytes (only even numbers allowed,  ie  word  boundary) 
after  both source and destination words,  which is  useful  when 
copying  a  single bit plane in low  or  medium  resolution.  The 
Blitter transfers data in lines,  and can also skip a set  number 
of  words at the end of each line - again,  this applies to  both 
source and destination.  The Blitter chip also allows the  source 
and  destination data to overlap,  so if necessary a  section  of 
memory can be read, manipulated and written back to the same area 
of memory

     When it is enabled, the Blitter is used by both GEM and some 
of the A-line routines, though not by the sprite routines. Use of 
the  Blitter in this way can be selected either from the  desktop 
by using the Blitter menu item or from within a program by  using 
Xbios call 64,  the blitmode call as found previously on the Mega 
ST. The Blitter can also be used directly, for example for custom 
graphics or sprite routines,  which although complex at first can 
produce fast graphics with less code.

---------
DMA Sound
---------
     The new DMA sound chip on the STE is in addition to, and not 
instead of, the original Yamaha PSG chip. The new hardware uses a 
digital  to analogue converter (DAC) to play 8-bit sound  samples 
at  one of four different frequencies,  from 6.25 to 50  kHz,  in 
either stereo or mono.  By comparison, CD players work at 47 kHz, 
but with 16-bit samples - this gives some idea of the quality  of 
the sound produced.

     The  sound  chip is another  DMA  device,  fetching  samples 
directly from memory for output.  This means that less  processor 
time is needed for sample playing, which is quicker and of better 
quality than with the original sound chip.

     Playing  a  sample is achieved by loading the  sound  chip's 
address  registers with the start and end address of  the  sample 
and  then setting the enable register to either play  the  sample 
once  or repeat it.  The DMA sound chip is connected to Timer  A, 
and this can be used in a similar way to the hblank interrupt  to 
play  a sample a specified number of times,  and to link  samples 
together to produce continous sound. The address registers on the 
sound chip are buffered,  allowing the address of the next sample 
to be set while a sample is playing,  thus allowing samples to be 
joined seamlessly.

     Comprehensive volume/tone control is also provided using the 
new  microwire interface connected to a  volume/tone  chip.  This 
allows master volume,  left and right volume, and bass and treble 
to  be set through software.  The sound output is via stereo  RCA 
jacks on the back of the machine,  ideal for connecting to a  hi-
fi.

     So far, the sound chip has been the best used feature of the 
STE,  with  many  samplers already compatible and more  and  more 
software  appearing with DMA sound as an option.  Hopefully  this 
feature of the STE will also be used in conjunction with MIDI and 
computer music, where the ST is almost standard.

---------------------------
Improved Video Shifter Chip
---------------------------
     The  STE's video shifter chip is an enhancement of  the  old 
chip,  providing access to a greater range of  colours,  vertical 
and  horizontal  hardware scrolling,  and accepting  an  external 
sync.

     The  colour  range has been increased from 512  to  4096  by 
using four bits instead of three to represent the red,  green and 
blue  components of each colour.  To maintain combatibility  with 
old machines,  the least significant bit of the new 4-bit  colour 
component  is  actually the most significant bit  in  the  colour 
nibble - if this were not so all 3-bit colour values from old STs 
would appear at half intensity as the maximum intensity was 7 and 
is  now  15.  This feature is useful for  graphics  applications, 
particularly scanning and video digitizing where a full 16  shade 
grey scale can be obtained (see 'User cover disc 56).

     Vertical  scrolling is achieved by allowing the screen  base 
to take any address,  rather than being on a 512 byte boundary as 
before.  This is done using an extra register for the low byte of 
the  screen address,  which does not affect the screen until  the 
next vertical blank.  This means the screen address can simply be 
changed to point to the next screen line,  giving smooth vertical 
scrolling.

     Horizontal scrolling is achieved through two new  registers. 
The  first sets the length of a screen line past the edge of  the 
screen,  allowing a screen in memory to be larger than the actual 
displayed screen.  This means screen data can be scrolled on from 
the sides of the screen.  The second register indicates which bit 
of  the  first screen word should be used as the first  pixel  on 
screen. This allows the screen to be bit scrolled horizontally up 
to 16 pixels,  at which point the base address can be changed  to 
continue scrolling.

     Using vertical and horizontal scrolling together to  produce 
four-way scrolling requires careful combination of both  methods, 
due to the different way the registers are used.  The  horizontal 
scrolling registers take effect immediately,  while the low  byte 
of the screen address is not used until the next vertical blank.

     Using the hardware scrolling on the STE,  smooth full colour 
full  screen  scrolling is possible with very  little  code,  and 
using only a small amount of processor time. However, this method 
usually requires more memory.

     The external sync input provided via the monitor port allows 
the STE's video shifter to synchronise with another device.  This 
is particularly useful in video genlocking, as the screen display 
can  be synchronised with video equipment,  and has already  been 
used on at least one such device.  Without this feature the video 
shifter chip often has to be prised out and a circuit board added 
to  allow the genlock to synchronise the computer with the  video 
device.

--------------
The Cookie Jar
--------------
     The  cookie  jar  is a welcome addition to  the  STs  system 
variables which provides a list of 'cookies', each of which gives 
some  information  about the features available on  a  particular 
machine.  This  information includes which CPU the  computer  has 
(68000 - 68040),  whether a Blitter chip is present,  whether the 
machine has DMA sound and which model the machine is. This allows 
applications  to  selectively  use these  features  if  they  are 
present,  and  should help with integrating STE features into  ST 
software.  Presumably  the  cookie jar has already been  used  in 
software which is STE compatible.

     Another  feature  of  the cookie jar is  the  provision  for 
applications  to  add their own cookies.  This means  that  other 
devices added to the ST can use the cookie jar to inform programs 
that they are present.

----------------
Controller Ports
----------------
     The  STE provides two new ports on the side of  the  machine 
which  can be used in a variety of ways.  The intended  uses  are 
either four standard joysticks (two per port),  two paddles or  a 
light pen or light gun. These ports are connected directly to the 
the 68000's bus,  instead of adding extra controller  chips,  and 
can  be  written as well as read.  The provision  of  four  8-bit 
Analogue  to Digital Converters (ADCs) for the paddles,  and  the 
fact  that the outputs are driven when the registers are  written 
to will no doubt give rise to other uses for these ports.

     Since the two ports both use 15-pin sockets adaptors will be 
needed  to connect most controllers.  How well used  these  ports 
become  depends largely on games designers and  programmers  (for 
joystick,  paddle or light gun use) and applications  programmers 
(for  light  pen  use) but the possibilities include  up  to  six 
player games,  analogue joysticks for flight simulators and light 
gun games.  Another possibility is the use of enhanced joysticks, 
perhaps with more than one fire button.

-----
SIMMS
-----
     RAM on the STE is on up to four Single Inline Memory Modules 
(SIMMs),  which can hold either 1/4 megabyte or 1 megabyte  each. 
These are easy to remove and install,  and are cheaper than other 
ST memory upgrades.  This allows the computer to be upgraded to 1 
megabyte  using  1/4 megabyte SIMMs or 4 megabytes  using  all  1 
megabyte  SIMMs.  Mixing the two sizes of SIMM is  possible,  but 
requires  extra  software to ensure the computer knows  how  much 
memory it has. SIMMs are easy to fit by simply removing the STE's 
lid and carefully clipping the SIMMs into place.

     It  is often possible to get cheap 1/4  megabyte  SIMMs,  as 
anyone   upgrading over 1 magabyte will have the old SIMMS  left. 
This  can make upgrading a 520 STE to one megabyte  cheaper  than 
buying  a  1040,  and may result in more software making  use  of 
extra memory,  particularly with the memory overheads  associated 
with sample playing and hardware scrolling.

-------------------
Programming the STE
-------------------
     The  rest  of this series of articles  will  concentrate  on 
programming the STE,  covering hardware  scrolling,  colour,  the 
Blitter  chip,  joystick  ports,  the cookie  jar  and  GEM,  and 
starting next month with DMA sound and volume/tone control.