-------------------------------------------------------------------------------

             ._____.  __     __ .______.  .______. ._.
            / .___. \ \ \   / / | .___. \ | .____! | |
            | |   !_!  \ \_/ /  | !___! | | !__.   | |
            | |   ._.   \   /   | .__. ./ | .__!   | |
            | !___! |    | |    | |  \ \  | !____. | !____.
            \._____./    !_!    !_!   \_\ !______! !______!

     .__   ._. ._.      ._. ._. .__    __. ._.            .____.
      \ \  | | !_!      | | !_! |  \  /  | !_! __    __  / .__. \
       \ \ | | ._.  .___| | ._. | . \/ . | ._. \ \  / /  | !__! |
        \ \| | | | / .__. | | | | |\  /| | | |  \ \/ /   | .__. |
         \ ! | | ! | !__! | | ! | | \/ | | | !  / /\ \   | !__! |
          \__| !_! \______! !_! !_!    !_! !_! /_/  \_\  \.____./


-------------------------------------------------------------------------------

 CyReL VIDIMIX-8 Features for SUNRISE M16-1280

 Version: 1.2b   Date:   02/93

-------------------------------------------------------------------------------

                               CyReL VIDIMIX-8

                     The Integrated Desk-Top Video Module
                        for the CyReL SUNRISE M16-1280
                       for the ATARI TT030 and MEGA STE

*  3 composite video inputs.
   Software allows to instantly switch between several video sources.

*  Software controllable 75 Ohm termination or high impedance for  
   loop-through on each input. Enables the operation of a control 
   monitor on each input or signal looping to the next video 
   processing station.

*  Inputs CCIR compatible. Almost any tape recorder, video disk, 
   Camcorder, Camera or video effects equipment can be used as a 
   video source.

*  1 composite video output. Accepted by most VCR and TV equipment.

*  1 S-VHS output ( MINIDIN-4 ) for better output quality and 
   signal fidelity.

*  Simultaneous S-VHS ( Y/C ) and NTSC / PAL output. Record the S-VHS 
   output while controlling the composite output on a monitor.

*  Programmable sync output ( high / low, composite, H & V ).
   Flexible enough to match any equipment requirements.

*  12 different NTSC & PAL output standards. Many different PAL and NTSC
   standards and options supported.

*  Interlaced / non-interlaced output possible. Captured interlaced video
   frames/clips can be played back in non-interlace mode for use on a
   computer monitor. Also de-interlaces incoming TV signals.

*  Pixel output configurable to 1:1 or 4:3 ratio. Ideal for switching
   between computer graphics (1:1) and video (4:3) applications.

*  Programmable 24-bit gamma correction. Allows many color correction
   functions as well as a host of special effects like solarisation.
   Software controlled color look-up table bypass feature. 

*  8 different YUV / RGB input formats. Process and save captured
   video frames and clips in many different formats including the
   most widely used YUV modes.

*  Video keying. Allows a wide range of 'graphics-over-video' effects,
   including video titling, GEN-locking and image keying.

*  Software controlled chrominance phase. Adjust the color quality of
   the output signal through software controlled slider functions.

*  Chrominace bandwidth enhancer. Boosts the output quality or reduces
   the signal strength to match any recording equipment specifications.

*  Software controlled color sub carrier adjust. Prevents loss of 
   color due to weak or mis-aligned color sub carrier frequencies.

*  Four operating modes ( including : Gen-lock, master / slave ).
   The VidiMix8 can either receive or generate all necessary control
   signals to drive a variety of video equipment.

*  Selectable fast tracking mode for VCR operation ( in Gen-lock mode ).
   Enables very stable gen-lock operation even when operating with
   various VCR playback modes.

*  Color or B&W operation. Introduce color to B&W pictures or convert
   color signals to black and white.

*  Background color generator. Flash fills the entire screen. Fades to
   or from any desired shade or black.

*  Real time true color digitizing. Digitizer can perform on-the-fly
   picture scaling. Scaling function and amount is software controllable.

*  Possible output resolutions :

  - NTSC  640 x 525  60Hz  interlaced
  - NTSC  720 x 525  60Hz  interlaced
  - PAL   720 x 625  50Hz  interlaced
  - PAL   768 x 625  50Hz  interlaced

  - NTSC  640 x 524  60Hz  non-interlaced
  - NTSC  720 x 524  60Hz  non-interlaced
  - PAL   720 x 624  50Hz  non-interlaced
  - PAL   768 x 624  50Hz  non-interlaced


-------------------------------------------------------------------------------

           Mail : Cybercube Research Ltd, 126 Grenadier Cres,
                  Thornhill, Ontario, Canada L4J 7V7
          Voice : (416) 882-0294  
            Fax : (416) 886-3261   
            BBS : (416) 882-5895
          GEnie : CYBERCUBE

Specifications subject to change without notice. All brand names
and trademarks are the property of their respective owners. 
Copyright (C)1993 by CYBERCUBE Research Limited

-------------------------------------------------------------------------------
<EOF>